ARPIE
Monophonic MIDI Arpeggiator
User Guide
Firmware rev A4, Hardware rev 2
September 2013

# Introducing ARPIE
ARPIE is a monophonic MIDI arpeggiator based around open-source software and hardware. The Arduino-based firmware enables simple code customisation and repurposing by users. The hardware is designed for easy DIY assembly and customisation.
Despite its simple construction and appearance, ARPIE is full featured with various chord arpeggiation and tempo synchronisation features, together with features to enable ARPIE to be used creatively without an attached MIDI keyboard.
A distinctive feature of ARPIE is the minimal control surface. While this has only simple LEDs for visual feedback, it is simple to use once you get familiar with it.
This manual is designed to provide a handy guide to using supplied ARPIE firmware and standard hardware. However it is not the full set of documentation available.
For information on troubleshooting, building, customising etc., as well as firmware updates, source code and hardware files please see https://github.com/hotchk155/arpie
# Quick Start
I know you just want to get started... So connect up your MIDI keyboard to MIDI in, and a sound module to MIDI out. Switch on the ARPIE.. after a short delay (1-2 seconds) the 16 blue data display LEDs should light and the CLK LED should start blinking.
Hold down a chord on the MIDI keyboard. The RX LED should blink as notes are received, and the TX LED should blink rapidly as notes are sent. Press the HOLD button once, the HOLD LED should illuminate. Now when you play a chord, the Arpeggiator continues to play after you have released the keys.
If you don't have a keyboard handy, turn on HOLD, press INST and then press the small button below the right-most blue LED. This should start playing a C major chord arpeggio.
OK, now we've broken the tension lets move on :o)
# Connections And Power
The rear panel of ARPIE is shown below:
The minimal requirements to make music with ARPIE are
- A synthesizer or other sound module connected to MIDI OUT
- A power source. This can be an internally mounted PP3 battery or a DC supply of between 9 and 24V connected to the rear 2.1mm, centre-positive socket. The socket automatically disconnects the battery when a plug is inserted.
Additionally, you can connect a MIDI controller to MIDI IN. Typically a piano type keyboard is used to play chords which provide input for ARPIEs arpeggiation engine however ARPIE can also be initialised with random or fixed chords without an external keyboard.
Optionally a MIDI clock source can be connected to MIDI SYNCH IN. For example you might want ARPIE to synchronise as a slave to a drum machine which can output a MIDI beat clock.
ARPIE can also slave to a MIDI beat clock on MIDI IN, though often the note controller and master clock sources will often be separate devices, which is where the external synch input is useful.
The main power switch is on the side of the device, close to the DC socket. Slide the switch toward the back of the unit to switch on power. The power LED (close to the switch) lights when power is on.
# The Control Surface
The top row contains three activity LEDs:
- The RX LED flickers when MIDI information is received via the input port
- The CLK LED - flickers at the start of each beat
- Then TX LED flickers when MIDI information being sent via the output port
The function of the Data Display LEDs and Data Entry Buttons depends on which of the function buttons was last pressed. Each function assigns specific meanings to each of the LEDs and Data Entry buttons. If no buttons are pressed for a few seconds the display function returns to Pattern Mode (PATN)
# HOLD
The HOLD button toggles the chord hold function on and off. This function means that a chord you press on a controller keyboard will continue to play after you release the keys. The HOLD feature also has some more subtle effects regarding sequencing and step timing, which are listed later.
An indicator LED beside the HOLD button shows when the chord hold function is in effect. If you press the HOLD button for more than a couple of seconds the LED will blink. The following table explains what each state of the LED means
Hold LED is	This means
OFF	Hold feature is off. / Press and release HOLD to activate the hold feature
ON (STEADY)	Hold feature is on / Press and release HOLD to deactivate the hold feature / Press and hold the button to enable MIDI transpose/lockout
BLINKING	If MIDI Transpose feature is ON then this means that note input from a MIDI keyboard will not change the content of the held arpeggio sequence but will instead transpose it up and down, according to the difference between the lowest note of the originally played chord and the newly pressed note. / If MIDI Transpose feature is OFF then MIDI lockout is activated. This means that the arpeggiator engine does not respond to any input from a MIDI keyboard. This can be useful when you have multiple ARPIEs in a MIDI chain and wish to control just one of them at a time.

# PATN
In this mode the sixteen data display LEDs show a pattern of “note” (LED on) or "rest" (LED off). You can toggle an LED on and off by pressing the data button below the LED.
This pattern of notes and rests and allows a rhythmic structure to be applied to the currently playing arpeggio. Arpeggiated notes are muted when they coincide with a rest in the pattern.
PATN is the default function, and the one to which ARPIE returns when you don't press anything for a while. You can return to this mode immediately by pressing PATN at any time.
# PLEN
This option changes the rhythmic pattern length. Press the PLEN button to view and change the length of the rhythmic pattern (from 1-16 steps). The current pattern length is indicated with a brighter LED and can be changed by pressing a data button.
The pattern restarts when it reaches the point defined by PLEN. This can be different from the length of the arpeggio sequence, allowing some interesting effects as the rhythmic pattern of notes and moves across the arpeggio sequence.
RHYTHMIC PATTERN LENGTH (STEPS)
1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16

# TYPE
This mode allows you to select the basic arpeggio type, controlling the way in which the Arp sequence is built from a chord. It also contains some buttons which can be used to initialise a pattern
ARPEGGIO TYPE					PATTERN
Up	Down	Up/Down	Random	Manual	Chord Gate					Random	Clear	Fill

ARP ORDER
- UP - notes of the chord are sorted into ascending order
- DOWN - notes of the chord are sorted into descending order
- UP-DOWN - notes of the chord are sorted into ascending, then descending order If the sequence spans multiple octaves, all octaves are spanned on the way "up" before returning "down". The highest note is not repeated.
- RANDOM - notes placed into a random order.
- KEYBOARD - notes of the chord are not reordered, so will be in the order they were received by MIDI.
PATTERN SETUP
- RANDOM - The rhythmic pattern (PATN mode) is randomised and its length (PLEN) is set to a random number.
- CLEAR - Pattern is cleared (all rests) and set to 16 step length.
- PATTERN FILL - Pattern is filled (all notes on) and set to 16 step length.
# SHFT
Octave shift the arpeggiated sequence (transpose it by whole octaves)
OCTAVE SHIFT
-2 Octaves	-1 Octave	None	+1 Octave	+2 Octaves

# SPAN
Determine the octave span (number of octaves the arpeggiated sequence will be extended over)
OCTAVE SPAN
1 Octave	2 Octaves	3 Octaves	4 Octaves	5 Octaves

# RATE
Determines the playback rate, by setting the length of notes in the arpeggiated sequence as a fraction of a beat (It does not alter the tempo/BPM)
ARPEGGIATED NOTE LENGTH
Full Beat	Dotted Half	Half Beat	Dotted Quarter	Quarter Beat	Dotted Eighth	Half Triplet	Eighth Beat	Quarter Triplet	Eighth Triplet	Dotted Sixteenth	Sixteenth Beat	Thirty-Second Beat	Sixteenth Triplet

# VELO
Controls the MIDI velocity of the notes output by the sequencer. There are two velocity modes and you can toggle between them by pressing and holding the VELO button.
Adjustable velocity mode allows you to override the velocity of all arpeggiated notes to one of 16 levels (including muted and full velocity) as indicated below
MIDI NOTE VELOCITY (SIXTEEN LEVELS INCLUDING MUTE/FULL)
Muted	1	2	3	4	5	6	7	8	9	10	11	12	13	14	Full Velocity

Original velocity mode plays each arpeggiated note using the velocity of the note as it was played in the chord on the input device. In this mode the data entry buttons have no function and only the right most LED is lit
# GATE
Controls the gate length of the notes output by the sequencer - as proportion of the current note length. The highest setting means that one note is "tied" to the next (The note is not stopped until the next note is started, with the MIDI note off message being sent after the next MIDI note on)
NOTE LENGTH AS FIFTEENTHS OF A STEP
1	2	3	4	5	6	7	8	9	10	11	12	13	14	Full Step	Tie Notes

# INST
Extends the length of the arp sequence by inserting repeated notes from the chord according to specific modes as defined below. This screen also has some options for inserting chords without a keyboard for demo purposes. The "Hold" switch must be enabled for this to work.
ARP INSERT / SLICE-DICE					REPLACE CHORD
None	Repeat Highest	Repeat Lowest	3 Fwd, 1 Back	4 Fwd, 2 Back	Slice-Dice 16 Steps	Slice-Dice 32 Steps	Slice-Dice 64 Steps			Random	Minor Seven	Major Seven	Seven	Minor	Major

# SYNC
This screen controls how the ARPIE synchronises its playback (standalone, or with other devices).
When ARPIE is running on its internal clock, the data display LED's indicate the approximate BPM. Pressing one of the nine BPM buttons sets the tempo to a specific value.
MODE			SEQUENCER TEMPO (BPM)					ADJUST
Source	Send		60	80	100	120	140	160	180	200	220		Tap Set	Faster	Slower

The SOURCE button controls the SYNCH clock source:
- ON – Internal clock source
- OFF – External clock source via the MIDI IN or SYNCH IN sockets
The SEND button controls whether ARPIE sends a MIDI beat clock to the MIDI OUT port. This button can also be used to start/stop and synchronise MIDI slave devices. More late rin the manual
- ON – Send MIDI synch messages out of MIDI OUT port
- OFF – Don't send MIDI synch messages
The BPM+ and BPM- buttons can be used to adjust the BPM by steps of 1.
Pressing the TAP button two or more times allows you to set the tempo interactively.
BPM defaults to 120 when ARPIE is switched on.
The internally generated BPM is approximate (but good enough for most stuff). However, an external clock source is recommended if a precise BPM is needed.

GLOBAL OPTIONS					SLIDE
Send Chan Msg	Pass Orig Notes	Pass Orig Chan Msg	Synch To MIDI In	Synch To SYNCH In					Backwards	Forwards	Set Startiung Point

# CHAN
When pressed, selects and displays the MIDI channel for output. Press an hold to set the input channel.
MIDI OUTPUT CHANNEL
1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16

If the CHAN button is pressed and held for a couple of seconds, you can Select The MIDI Input Channel. By default ARPIE will accept input from any MIDI channel (OMNI mode) but you can also select a specific channel, which affects MIDI Thru behaviour (see below)
OMNI mode is indicated by all the Data Display LEDs showing brightly. Pressing any single button will select an individual input channel. Pressing the same button again will restore OMNI mode.
MIDI INPUT CHANNEL
1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16

# TRAN - note transpose
Transpose the MIDI output. Buttons represent -3. -2, -1, 0, +1, +2 through to +12 semitones. The default (no shift) position is indicated with a brighter LED.
NOTE TRANSPOSE (SEMITONES)
(-) 3	(-) 2	(-) 1	None	(+) 1	(+) 2	(+) 3	(+) 4	(+) 5	(+) 6	(+) 7	(+) 8	(+) 9	(+) 10	(+) 11	(+) 12

FORCE TO SCALE					TRANS.LOOP
Off (Chromatic)	Ionian Mode	Dorian Mode	Phyrigian Mode	Lydian Mode	Mixolydian Mode	Aeolian Mode	Locrian Mode		Off	16 Steps / Rec / Play	32 Steps / Rec / Play	64 Steps / Rec / Play			MIDI Transpose Enable

# More About HOLD
Here is everything you wanted to know about the hold button. And some more.
HOLD is OFF	One or more keys are pressed and held	Arpeggiation starts from beginning of pattern and plays immediately. Beat time is reset
	One or more keys are released from a chord but at least one key remains held	Arpeggio is rebuilt but position in pattern and timing of next beat are unaffected
	One or more additional keys are pressed while a chord is held
	Final key is released	Arpeggiation stops
	HOLD pressed while keys are held	HOLD is ON using the current chord. Pattern position and next beat time are unaffected
HOLD / is ON	One or more keys are initially pressed	Arpeggiation starts from beginning of pattern. Next beat timing is unaffected so the first step plays according to the current beat time
	Some keys are released from the chord	No effect. The released keys remain in the arpeggio
	Additional keys are pressed while at least one key of the chord remains held	Arpeggio is rebuilt but position in pattern and timing of next beat are unaffected
	All keys are released	No effect
	One or more keys pressed after releasing all keys of the previous chord	Arpeggio is replaced but position in pattern and timing of next beat are unaffected
	HOLD pressed while keys remain held	All notes removed from the arpeggio except any that are still physically pressed on keyboard. HOLD is OFF
	HOLD pressed while no keys are held	Arpeggiation stops. HOLD is OFF

# More about synch
SOURCE	SEND
INTERNAL / (LED is ON)	OFF	STANDALONE / Running on internal beat clock / Internal beat clock is not sent to MIDI output / Incoming synch messages are ignored
	ON	MASTER / Running on internal beat clock / Incoming synch messages are ignored / Internal beat clock is sent to MIDI output / When SEND goes from OFF-ON the beat clock is restarted and MIDI restart message is sent to downstream devices / When SEND goes from ON-OFF the beat clock is stopped and a MIDI stop message is sent to downstream devices
EXTERNAL / (LED is OFF)	OFF	SLAVE / Requires external synch / Both MIDI IN and SYNCH IN are active (but only one should be used to receive synch messages at any time) / Incoming synch messages are not passed to output
	ON	SLAVE + THRU / Requires external synch / Both MIDI IN and SYNCH IN are active (but only one should be used to receive synch messages at any time) / Incoming synch messages are not passed to output

# More About MIDI Thru
Input Channel Mode	Behaviours
OMNI mode (default)	MIDI note on/note off messages from any input channel are passed to the arpeggiator engine and are not passed to the output
	Other MIDI channel messages (such as pitch-bend and mod-wheel) are passed through to output but the channel is always changed to equal ARPIEs selected output channel
	Incoming MIDI beat clock message are only passed to output if SYNCH SOURCE is EXTERNAL and SYNCH SEND is ON
	Other Realtime/SysEx are passed through
Specific Input Channel	MIDI note on/note off messages from the specific input channel are passed to the arpeggiator engine and are not passed to the output
	MIDI note on/note off messages for other channels are passed are passed through to output on their original channels
	Other MIDI channel messages (such as pitch-bend and mod-wheel) are passed through to output on their original channels
	Incoming MIDI beat clock messages are only passed to output if SYNCH SOURCE is EXTERNAL and SYNCH SEND is ON
	Other Realtime/SysEx are passed through

MIDI thru is handed in ARPIEs firmware (there is no hardware thru) which can cause latency if the arpeggiator engine is busy - and possibly even dropped messages in situations of very high thru volume.
# Stored settings
ARPIE stores the following settings in EEPROM, which means that they are remembered when the device is switched off, and used as defaults next time it is switched on
- Synch SOURCE setting
- Synch SEND setting
- MIDI input channel (or OMNI) setting
- MIDI output channel setting